## Slide 1
WEBINAR: PYLEECAN BASICS
PYthon Library for Electrical Engineering Computational ANalysis
Pierre Bonneel – pierre.bonneel@eomys.com
Hélène Toubin – helene.Toubin@eomys.com
Raphaël Pile – raphael.pile@eomys.com
Pr. Fabrizio MARIGNETTI from University of Cassino, AEIT
16th October 2020

## Slide 2
  1: How to use pyleecan (pyleecan basics, FEMM, GUI)
  Friday 16 Oct 15:00-17:00 (GMT+2)
  2: How to use pyleecan (advanced) (Optimization, mesh, plot)
  Friday 30 Oct 15:00-17:00 (GMT+1)
  3: How to contribute to pyleecan (Github, OOP)
  Friday 6 Nov 15:00-17:00 (GMT+1)
WEBINAR ORGANIZATION
2
Notes: Mute for all
Question in chat to host
Use Q/A

## Slide 3
WEBINAR ORGANIZATION
Webinar n°1: How to use pyleecan – Basics
What is pyleecan ?
How to define a machine with pyleecan ?
How to run the Magnetic module ?
How to iterate on several Operating Point ?
How to run the Electrical module ?
  To follow the Webinar, please go to
  https://pyleecan.org/tutorials.html
3

## Slide 4
EOMYS ENGINEERING
Founded in 2013 in Lille, North of France (1 hour from Paris)
Activities : engineering consultancy in electrical engineering, specialized in noise and vibrations of electrical systems
14 R&D Engineers (electrical engineering, vibro-acoustics, scientific computing)
MANATEE: commercial software for electromagnetic and vibro-acoustic analysis of electrical machines
3 active projects in opensource software: PYLEECAN, MOSQITO, SciDataTool
4

## Slide 5
Pyleecan origins
Open-source
for research
Commercial
software
New version of MANATEE software in Python with a new OOP architecture
New OOP architecture opens lots of research possibilities
=> PYLEECAN introduced in a publication at ICEM 2018
electromagnetics and vibro-acoustics
5

## Slide 6
GREEN FORGE COOP
Green Forge Coop (GFC) is a non-profit organisation supporting open-source software for energy transition and sustainable development
6
GFC supports the development of PYLEECAN and MOSQITO
Founded by some members of EOMYS to split the management of PYLEECAN and to enable anyone to join the project

## Slide 7
What is Pyleecan?
open-source
user-friendly
flexible simulation framework
multiphysic design
electrical machines and drives
optimization
7

## Slide 8
What is Pyleecan: “Open Source”
The first aim of PYLEECAN is to encourage reproducible and collaborative applied research in electrical machines design
The code must be accessible for everyone to read, use and contribute The code must be developed using the mostly used free scientific language
Apache Licence 2.0
Python 3.0 Largest scientific community Boosted by big data & AI trends IDE as user-friendly as Matlab Large number of scientific libraries
Jupyter notebooks
Cf. PYLEECAN ICEM 2018 publication for more details
8

## Slide 9
What is Pyleecan: “flexible simulation framework”
The architecture of PYLEECAN is organized with « Object Oriented Programming »
The objective of the architecture is to encapsulate most of the code in « object / interfaces »
comp_height
returns H0+H1+H2
comp_height
returns H0+H2
A slot object
With comp_height
method
A different slot object
With a different
comp_height method
The second aim of PYLEECAN is to boost applied research on innovative topologies and models of electrical machines
9

## Slide 10
What is Pyleecan: “flexible simulation framework”
In PYLEECAN everything is an object (topologies, model, post-processing…)
=> Simple to add new topologies
=> Simple to add new model
=> Simple to compare several model and/or topologies
=> All the work done around a model is automatically reusable for any new model
Magnetic model object
With a run method
Magnetic output object
With dedicated
Post-processing
Structural model object
With a run method
Magnetic model object
With a run method
10

## Slide 11
What is Pyleecan: “electrical machines”
A machine is a composition of several objects (laminations, magnet, winding…)
A new machine can be easily assembled with a set of objects
Initial scope: simulate electromagnetic performances main 2D radial flux machines with inner or outer rotor: - Interior, Surface & Surface Inset Permanent Magnet Synchronous Machines (IPMSM, SPMSM, SIPMSM) - Squirrel Cage Induction Machines (SCIM) and Doubly Fed Induction Machines (DFIM) - Synchro Reluctant Machines (SynRM) - Switched Reluctance Machines (SRM)
Topological extension can be done to linear motors or axial flux motors (contributions welcome !)
11

## Slide 12
What is Pyleecan: “electrical machines” – SOME MORE EXOTIC EXAMPLES
0
0
12
Cf. PYLEECAN ICEM 2020 publication for more details

## Slide 13
What is Pyleecan: “Multiphysic simulation”
Electromagnetic module with FEMM coupling
3D mesh generation with gmsh as a first step for structural module
ELECTROMAGNETIC MODULE
ELECTRICAL MODULE
STRUCTURAL MODULE
Machine object
THERMAL MODULE
TBD
TBD
13

## Slide 14
What is Pyleecan: “User Friendly” – tutorials & GUI
GUI to define all kinds of e-machine + edit material library
Website with documentation and tutorials
14

## Slide 15
What is Pyleecan: “User Friendly” - SCRIPTING AND POST PROCESSING
0
Development can be carried under Anaconda/Spyder with same layout as Matlab:
Files & folders
Plot viewer
Variable Explorer
Help
Scripting/library loading
Scripting: stator + slot + winding definition method call to plot MMF
15

## Slide 16
What is Pyleecan: “User Friendly” - SCRIPTING AND POST PROCESSING
0
pyleecan imports SciDataTool features to post process & visualize scientific data in space and time/frequency domain
16

## Slide 17
What is Pyleecan: “Optimization”
Optimization module:
- Multi-objective problem under constraints
- Discrete and continuous design space
- NSGA-II genetic algorithm
Example :
Vary slot opening width and magnet width
Maximize average torque and minimize torque ripple
17

## Slide 18
Pyleecan & ENERGY-EFFICIENCY
Pyleecan project is backed by a non-profit association called Green Forge Coop
Ethical chart: a catalyst for research in electrical machines applied to sustainable mobility and energy production, towards more efficient, environmental-friendly electrical drives
Sub-optimized electric motors are still put in production due to high cost of commercial FEA software
Loss modelling is an active research field (e.g. impact of manufacturing on lamination eddy current losses, impact of space harmonics on magnet losses, proximity effects)
Although automotive driving cycles are standardized, loss computing methods are not made public and far from reproducible science
-> there is a strong need of an open source modelling & simulation framework for energy-efficient electrical machines and drives
18

## Slide 19
Pyleecan & ENERGY-EFFICIENCY
Need to implement state of the art loss models with laboratories:
- winding copper losses (proximity effects, skin effect, PWM time harmonics) - lamination iron losses (eddy current, hysteresis losses, etc) - magnet losses (effects of segmentation, space harmonics)
Pyleecan naturally allows to include different granularity models (analytical, semi-analytic, numeric)
Automated coupling with FEMM allows to gather all flux density values in lamination, magnets etc…
19

## Slide 20
WHY USING PYLEECAN iN your lab / R&D DEPARTMENT?
High modeling & simulation flexibility to handle innovative topologies of e-machines and drives
Based on the mostly used scientific language Python with access to latest development in AI, optimization and big data analysis
Possibility to share scripts and development work among several laboratories and R&D department for an improved knowledge management
Reliable software with open validation cases, active user community, detailed documentation
Easy post-processing and visualization of simulation results (SciDataTool & Spyder IDE)
Cost-competitive solution for multiphysic design optimization of electric machines & drives
Boosts reproducible science for more efficient and reliable research work
20

## Slide 21
CONCLUSIONS
Ideally, every PhD and researcher should start scripting new e-machines under PYLEECAN instead of scripting a coupling between FEMM and Matlab/Scilab… Subscribe to our newsletter on www.pyleecan.org Looking forward to further collaboration with industries & laboratories! Join our development effort on https://github.com/Eomys/pyleecan Next webinar Friday 30 Oct 15:00-17:00 (GMT+1) Webinar videos will be made available at https://pyleecan.org/media.html#
21